## Slide 1: Multifidelity Aeroelastic Optimization: Bibliographic Study
Author:
Giovanni QUAGLIA
Supervisors:
Pr. Joseph MORLIER
Pdf. Joan MAS COLOMER
21/05/2019

## Slide 2: Context
COMPLEX MODEL
The reduction of computational cost is a subject of major interest in aircraft design.
Solution approaches: Multifidelity and Surrogate Models.

## Slide 3: Summary
Black Box Aeroelastic Function
Multifidelity
Surrogate Models
  Kriging
  Co-Kriging
Optimization
SEGOMOE Framework
Future Work

## Slide 4: Black Box Aeroelastic Function
Fluid-Structure interaction problem is solved in an iterative partitioned approach.
OpenMDAO Model
Two separate aerodynamics and structural software are coupled together in a unique function.

## Slide 5: Multifidelity
The employment of functions with different accuracy and computational time can speed up the design process.
Examples:
High and Low fidelity software
Relaxed convergence criterion
Various mesh resolutions
Experiments

## Slide 6: Surrogate Model
Computational cost is decreased analyzing a surrogate model of the real function.
DOE Sampling
Ex. LHS
Interpolation
Ex. Kriging, Co-Kriging

## Slide 7: Surrogate Model
Kriging interpolation fits data to a Gaussian Process with constant mean and a defined covariance.
Uncertainty on the prediction is zero in the sampled points and increases with distance.

## Slide 8: Surrogate Model
Co-Kriging interpolation takes into account data from two sources of different fidelity.
The prediction is based on the error between the High and Low Fidelity models.
Then a lower number of HF evaluations is required to build the surrogate model.

## Slide 9: Optimization
Variable optimization can be performed on the surrogate model.
The optimum research balances exploration and exploitation considering the model uncertainty.
Prediction
Expected Improvement
Probability

## Slide 10: SEGOMOE Framework
ISAE Supaero and ONERA developed the SEGOMOE Framework in a joint project:
Multifidelity samples are clustered under different surrogate models (MFK, KPLS(-K), RBS, PA2, PA3, …)
Clusters are merged by a EM algorithm in a Gaussian Mixture Model
WB2 optimum criterion
The framework is currently tested on the NASA CRM concept.

## Slide 11: Future Work
PIR Planning:
May
June
Bibliographic research
21 May: bibliographic presentation
Create a CRM Low fidelity structural model
Development of a more general structural simplification algorithm
PIR final presentation

## Slide 12: References
[Bartoli et al., 2016] Bartoli, N., Kurek, I., Lafage, R., Lefebvre, T., Priem, R., Bouhlel, M. A.,
Morlier, J., Stilz, V., and Regis, R. (2016). Improvement of efficient global optimization with mixture of experts: methodology developments and preliminary results in aircraft wing design.
[Mas-Colomer, 2018] Mas-Colomer, J. (2018). Aeroelastic Similarity of a Flight Demonstrator via
Multidisciplinary Optimization. PhD thesis.
[Jones et al., 1998] Jones, D. R., Schonlau, M., and Welch, W. J. (1998). Efficient global optimization
of expensive black-box functions. Journal of Global Optimization, 13(4):455–492.
[Scholcz, 2015] Scholcz, T. (2015). Multi-fidelity methods for fluid-structure interaction and uncertainty
quantification.
[Jones, 2001] Jones, D. R. (2001). A taxonomy of global optimization methods based on response
surfaces. Journal of Global Optimization, 21(4):345–383.
[Forrester et al., 2007] Forrester, A. I., Sóbester, A., and Keane, A. J. (2007). Multi-fidelity optimization via surrogate modelling. Proceedings of the Royal Society A: Mathematical, Physical and Engineering Sciences, 463(2088):3251–3269.

## Slide 13: Thanks for your attention!
Any questions?